# Quiz Review
## Question 1
Didn't use secondaries on the power transformers. This makes it used as an autotransformer.
DIAGRAM
Can find autotransformers in rural areas, like a transmitter remotely located on a mountain.
## Question 2
### Advantages
No DC, so would not be any DC to block.
Isolation provided.
Can use two 10:1 transformers if don't have a 1:1 available.
### Disadvantages
Would have to have substantial size transformers for high current.
Would have a voltage drop and IR losses with a long line in the 12V section.
## Question 3
DIAGRAM
## Question 4
CT = C1 C2 / (C1 + C2)
Answer will be less than the capacitance of the smallest capacitor.
Capacitors in series combine like resistors in parallel.
## Question 5
Answer will be less than the resistance of the smallest resistor.
RT = 1 / ((1 / R1) + (1 / R2) + (1 / R3))
## Question 6
What is IT for #5? I = E / R = 12/91 = .13A
## Question 7
What is total power (PT)? P = EI = (12) (.13) = 1.6 watts
## Question 8
Voltage across R1? Same as across all the other resistors (12V).
## Question 9
Draw an integrator and show the output waveform with a square wave input.
This question is under review. The answer given is for a differentiator circuit.
## Question 10
Skip this – see question 9.
## Question 11
What is resonance? In a circuit with a capacitor and an inductor, at a specific frequency, when XC = XL (when inductive reactance equals and is opposite to capacitive reactance).
## Question 12
Xc for 100 mF, 120V, t=5? After 5 time constants, the capacitor is considered to be fully charged, so no current flow since there is no AC and the capacitor is charged, capacitive reactance is infinite (approaches infinity).
## Question 13
The capacitor would attenuate the flow of the lower frequency signal through the capacitor, but it would attenuate the flow of the higher frequency signal around the capacitor (in the case where the output of the circuit is taken across the capacitor). Capacitors will pass higher frequency signals because capacitive reactance is inversely proportional to frequency (i.e., high frequency, low capacitive reactance).
## Question 14
Ohms.
## Question 15
Reactance is frequency-sensitive, resistance is not.
## Question 16
The square root of -1.
## Question 17
C = 80 nf, f = 42 Hz. The abbreviation nF stands for nanofarads (10 -9 farads).
Xc = 1 / (2 pi f C) = 1 ( 2 * pi * 42 * 80 * 10-9) = 47k ohms.
## Question 18
Increases
## Question 19
I leads E by 90 degrees for capacitive reactance circuits. Recall ELI the ICE man as a mnemonic phrase. ICE means that I leads E for Capacitive reactance circuits.
## Question 20
Hybrid transformer converts 2-wire to 4-wire.
# Transistors
Will discuss transistor amplifier configurations.
## Configurations
### Common Emitter
Most widely used configuration.
Advantages: current, voltage, and power gain.
180 degree phase shift between input and output.
DIAGRAM
Neither input nor output flows through the emitter.
Can be used for comb filtering.
### Common Base
Low input impedance, high output impedance.
No phase shift between input and output.
DIAGRAM.
### Common Collector
Also known as emitter follower.
High input impedance, low output impedance.
No phase shift between input and output.
Used in video circuits, for example, when going out to 75 ohms output.
DIAGRAM
### Additional
Can use Common Emitter and Common Collector simultaneously.
DIAGRAM
## History
1948 – June 30th – when transistor first introduced/reported.
John Pierce at Bell Labs.
Transistor = transfer resistor.
First transistor large, didn't handle much current.
Became popular in the mid-1960's.
## Advantages of Transistors over Tubes
Smaller size.
Generate less heat.
No warmup time.
More durable.
Could use a lot lower DC voltage in transistor circuits.
Portable tube radios required three batteries: heater, plate, bias.
## Joke
“transistor put in circuit to protect the fuse” - an example of Murphy's law
## Categories
### Bipolar
NPN or PNP. NPN is used more often because of noise – they are quieter.
### Field Effect (FET)
Terminals are gate, drain, source.
DIAGRAM of schematic symbol for FET.
Has a substrate connecting drain and source. The gate constricts flow through electrostatic field.
FET is higher impedance than bipolar. Found where don't want a lot of load on the circuit, like capacitive circuits where resistance of the capacitor is significant.
Types include MOSFET (metal oxide silicon) and JFET (junction).
# End Notes
Remainder of transistor lecture on Tuesday.
Moving away from discrete components toward integrated components.