# Homework
Diagram 1
SMPTE time code Manchester encoding. Zero defined as no transition within a clock frame. One is defined as a transition within a clock frame.
Put data in, come out with a clock that is synchronous with our data.
Clock can be any multiple of the base frequency.
If sample ¼ of the way into the cycle, and ¾ of the way into the cycle, if there are different values at the two sample times, there is a 1 encoded, otherwise there are no differences between the two sample times and there is a 0 encoded.
The output data will actually be delayed/shifted by one clock cycle since we have to read the voltages during most of the cycle before we can decode the value.
Recall that a number of the complex chips we use are leading-edge-triggered, so would need to multiply the clock by 4 in order to get 4 edges within each 2400 Hz cycle so one can sample at ¼ and ¾ cycle.
Will grade papers today. If don't get it right, will have a chance to turn it in Thursday for a bit less credit.
# Lab
Mostly spent time in lab today.