# Previous Quiz
Define potential difference. Voltage.
Define electromotive force. Voltage.
A condenser may also be called what? Capacitor.
C = KA/t. What are we calculating? Capacitance. How do I find K? K = tC/A. What is t? Distance between plates or thickness of dielectric.
Which electronic component will act like a firecracker if connected to the proper voltage but in reversed polarity (be specific)? Electrolytic capacitor. Some rare costly electrolytic capacitors are non-polarized; used in speakers in crossovers, since handles AC. Take two electrolytic capacitors back to back, connect negative leads together, make a non-polarized electrolytic capacitor.
Q = CE. What are we calculating? Charge in coulombs that a capacitor would hold. What is C? Capacitance. What is Q? Charge in coulombs.
# Quiz
Timed quiz, until 3 PM.
# Assignments
Look on oscilloscope sites (Tek, Leader). Write a report on all controls on the oscilloscope. Due Thursday.
Turn in corrections for the quiz on Tuesday.
# Projects